## Slide 1
G. A. ‘Mac’ McLean, Ph.D.
David B. Weed, M.A.
Protection and Survival Research Laboratory
FAA Civil Aerospace Medical Institute
Oklahoma City, OK 73125
Identification and Comprehension of Symbolic Exit Signs for Small Transport Category Airplanes
Federal Aviation
Administration

## Slide 2
14CFR 25.811 – Emergency Exit Marking
(d) (1) A sign located above the aisle
(2) Next to each exit
(3) On each obstructing bulkhead or divider
14CFR 25.812 – Emergency Lighting
(a) (1) Illuminated emergency exit marking and locating signs
(b)(1) (i) Red letters 1.5” high on white background, 21 sq in., stroke width between 6 and 7:1 contrast ratio 10:1, 25 ft. Lamberts,
internally illuminated w/high to low background contrast < 3:1.
Required Emergency Exit Sign

## Slide 3: Symbolic Exit Sign
14CFR 21.21- Issue of Type Certificate
(b)(1) the type design and product [must] meet the applicable airworthiness requirements of the Federal Aviation Regulations or… any provisions not complied with [must be] compensated for by factors that provide an equivalent level of safety.

## Slide 4: Non-Contextual Symbols

## Slide 5
Category | Response Type | Weight
0 | No response | 
1 | Don’t Know | 
2 | Opposite to the intended meaning | - 1.00
3 | Wrong | 0.00
4 | Related but understanding is doubtful / suspect | 0.25
5 | Related but understanding is arguable | 0.50
6 | Understanding is likely | 0.75
7 | Understanding is certain | 1.00
Comprehension Response Categories & Weights

## Slide 6: Exit Here

## Slide 7: Exit Here

## Slide 8: Exit Here

## Slide 9: Exit Straight Ahead

## Slide 10
Non-Contextual Comprehension Score Comparison

## Slide 11: Contextual Symbols

## Slide 12: Exit Here
Chart: Comprehension Score = 74.9%
| 0 | 1 | 2 | 3 | 4 | 5 | 6 | 7
 | 7 | 7 | 3 | 26 | 8 | 23 | 16 | 158

## Slide 13
Exit Straight Ahead
Chart: Comprehension Score = 63.7%
| 0 | 1 | 2 | 3 | 4 | 5 | 6 | 7
 | 2 | 1 | 0 | 19 | 4 | 12 | 3 | 43

## Slide 14: Exit Both Sides
Chart: Comprehension Score = 71.8%
| 0 | 1 | 2 | 3 | 4 | 5 | 6 | 7
 | 1 | 0 | 0 | 16 | 2 | 2 | 15 | 44

## Slide 15: Contextual Comprehension Score Comparison

## Slide 16: Context-Based Conclusions
Traditional Part 25.811 / .812 EXIT Sign Universally Understood
Symbolic Signs Without Context Had Mean Comprehension of About 50%
Addition of Contextual Cues Improved Mean Comprehension to About 70%
Symbolic Signs Were Shown NOT to be Equivalent to Traditional EXIT Sign
Additional Compensating Factors Would be Required to Establish an
Equivalent Level of Safety

## Slide 17: Signs for Small Transport Category Airplanes

## Slide 18
14CFR 25.811 – Emergency Exit Marking
(d) (1) A sign located above the aisle
(2) Next to each exit
(3) On each obstructing bulkhead or divider
14CFR 25.812 – Emergency Lighting
(a) (1) Illuminated emergency exit marking and locating signs
(b)(2) Red letters 1.0” high on white background at least 2.0” high, internally or self illuminated at an initial minimum of at least 160 microlamberts.
Required Emergency Exit Sign

## Slide 19: Paper Booklet Exit Sign Test

## Slide 20: Approved Symbolic Exit Sign Featuring the ISO 7010:2011 Running Man with Narrow Arrows

## Slide 21: Proposed Symbolic Exit Sign Featuring a Modified ISO 7010:2011 Running Man with ISO 3864-3:2012 (E) Wide Arrows

## Slide 22: Alternate Signs
First Aid Kit Ahead
Do Not Enter: Biohazard
Caution / Attention: Radiation
Gas Mask Must Be Worn

## Slide 23: Visual Acuity Chart

## Slide 24: Test Area and Booklet Viewed from 32 Feet

## Slide 25: Test Booklet B
Gas Mask Must Be Worn
Do Not Enter: Biohazard
Modified Green Man with Narrow Arrows
Attention / Caution: Radiation
First-Aid Kit with Wide Arrows

## Slide 26: Cumulative Identification of Arrow Elements

## Slide 27: Cumulative Identification of Running Man Elements

## Slide 28: Comprehension Response Categories & Weights
Category | Response Type | Weight
0 | No response | 
1 | Don’t Know | 
2 | Opposite to the intended meaning | - 1.00
3 | Wrong | 0.00
4 | Related but understanding is doubtful / suspect | 0.25
5 | Related but understanding is arguable | 0.50
6 | Understanding is likely | 0.75
7 | Understanding is certain | 1.00

## Slide 29: Comprehension of ISO Running Man with Narrow Arrow Elements
Comprehension Category | Frequency | Percent | Weight | Comprehension Score
Certain | 1 | 4.00 | 1.00 | 4.00
Likely | 8 | 32.00 | 0.75 | 24.00
Arguable | 5 | 20.00 | 0.50 | 10.00
Suspect | 4 | 16.00 | 0.25 | 4.00
Opposite | 0 | 0.00 | -1.00 | 0.00
Wrong | 7 | 28.00 | 0.00 | 0.00
Total | 25 | 100.00 |  | 42.00

## Slide 30: Comprehension of Modified Running Man with Wide Arrow Elements
Comprehension Category | Frequency | Percent | Weight | Comprehension Score
Certain | 0 | 0.00 | 1.00 | 0.00
Likely | 9 | 36.00 | 0.75 | 27.00
Arguable | 5 | 20.00 | 0.50 | 10.00
Suspect | 5 | 20.00 | 0.25 | 5.00
Opposite | 1 | 4.00 | -1.00 | -4.00
Wrong | 5 | 20.00 | 0.00 | 0.00
Total | 25 | 100.00 |  | 38.00

## Slide 31: Comprehension of Modified Running Man with Narrow Arrows
Comprehension Category | Frequency | Percent | Weight | Comprehension Score
Certain | 0 | 0.00 | 1.00 | 0.00
Likely | 7 | 28.00 | 0.75 | 21.00
Arguable | 5 | 20.00 | 0.50 | 10.00
Suspect | 6 | 24.00 | 0.25 | 6.00
Opposite | 0 | 0.00 | -1.00 | 0.00
Wrong | 7 | 28.00 | 0.00 | 0.00
Total | 25 | 100.00 |  | 37.00

## Slide 32: First Aid Kit Ahead
Comprehension Category | Frequency | Percent | Weight | Comprehension Score
Certain | 0 | 0.00 | 1.00 | 0.00
Likely | 22 | 29.33 | 0.75 | 22.00
Arguable | 18 | 24.00 | 0.50 | 12.00
Suspect | 15 | 20.00 | 0.25 | 5.00
Opposite | 0 | 0.00 | -1.00 | 0.00
Wrong | 17 | 22.67 | 0.00 | 0.00
None | 3 | 4.00 | 0.00 | 0.00
Blank | 0 | - | - | 0.00
Total | 75 | 100.0 |  | 39.00

## Slide 33: Caution / Attention: Radiation
Comprehension Category | Frequency | Percent | Weight | Comprehension Score
Certain | 8 | 10.67 | 1.00 | 10.67
Likely | 18 | 24.00 | 0.75 | 18.00
Arguable | 7 | 9.33 | 0.50 | 4.67
Suspect | 16 | 21.33 | 0.25 | 5.33
Opposite | 0 | 0.00 | -1.00 | 0.00
Wrong | 19 | 25.33 | 0.00 | 0.00
None | 7 | 9.33 | 0.00 | 0.00
Blank | 0 | - | - | 0.00
Total | 75 | 100.0 |  | 38.67

## Slide 34: Gas Mask Must Be Worn
Comprehension Category | Frequency | Percent | Weight | Comprehension Score
Certain | 5 | 10.00 | 1.00 | 10.00
Likely | 4 | 8.00 | 0.75 | 6.00
Arguable | 7 | 14.00 | 0.50 | 7.00
Suspect | 18 | 36.00 | 0.25 | 9.00
Opposite | 0 | 0.00 | -1.00 | 0.00
Wrong | 6 | 12.00 | 0.00 | 0.00
None | 10 | 20.00 | 0.00 | 0.00
Blank | 0 | - | - | 0.00
Total | 50 | 100.0 |  | 32.00

## Slide 35: Do Not Enter: Biohazard
Comprehension Category | Frequency | Percent | Weight | Comprehension Score
Certain | 5 | 6.67 | 1.00 | 6.67
Likely | 6 | 8.00 | 0.75 | 6.00
Arguable | 12 | 16.00 | 0.50 | 8.00
Suspect | 21 | 28.00 | 0.25 | 7.00
Opposite | 0 | 0.00 | -1.00 | 0.00
Wrong | 20 | 26.67 | 0.00 | 0.00
None | 11 | 14.67 | 0.00 | 0.00
Blank | 0 | - | - | 0.00
Total | 75 | 100.0 |  | 27.67

## Slide 36: Self-Illuminated Exit Sign Test

## Slide 37: Proposed Symbolic Exit Sign Featuring a Modified ISO 7010:2011 Running Man with ISO 3864-3:2012 (E) Wide Vertical Arrows

## Slide 38: Proposed Symbolic Exit Sign Featuring a Modified ISO 7010:2011 Running Man with ISO 3864-3:2012 (E) Wide Horizontal Arrows

## Slide 39: ISO 7010:2011 Automatic External Defibrillator and Narrow ISO 3864-3:2012 (E), Type D Arrows

## Slide 40: Visual Acuity Charts Displayed on Side Test Track

## Slide 41: Test Track and Signs Viewed From 45 Feet

## Slide 42: Cumulative Identification of Sign Elements in the Dark (0.00 fc)

## Slide 43: Cumulative Identification of Sign Elements in Emergency (0.05 fc) Lighting

## Slide 44: Cumulative Identification of Sign Elements in Low (0.50 fc) Lighting

## Slide 45: Cumulative Identification of Sign Elements in High (45 fc) Lighting

## Slide 46: Cumulative Identification of Sign Elements in All Lighting Conditions

## Slide 47
Comprehension Category | Frequency | Percent | Weight | Comprehension Score
Certain | 10 | 40.00 | 1.00 | 40.00
Likely | 3 | 12.00 | 0.75 | 9.00
Arguable | 2 | 8.00 | 0.50 | 4.00
Suspect | 4 | 16.00 | 0.25 | 4.00
Opposite | 0 | 0.00 | -1.00 | 0.00
Wrong | 6 | 24.00 | 0.00 | 0.00
None | 0 | 0.00 | 0.00 | 0.00
Total | 25 | 100.0 |  | 57.00
Comprehension of Exit Signs In Dark (0.00 fc) Lighting

## Slide 48
Comprehension Category | Frequency | Percent | Weight | Comprehension Score
Certain | 14 | 56.00 | 1.00 | 56.00
Likely | 1 | 4.00 | 0.75 | 3.00
Arguable | 5 | 20.00 | 0.50 | 10.00
Suspect | 4 | 16.00 | 0.25 | 4.00
Opposite | 0 | 0.00 | -1.00 | 0.00
Wrong | 1 | 4.00 | 0.00 | 0.00
None | 0 | 0.00 | 0.00 | 0.00
Total | 25 | 100.0 |  | 73.00
Comprehension of Exit Signs In Emergency (0.05) fc Lighting

## Slide 49
Comprehension Category | Frequency | Percent | Weight | Comprehension Score
Certain | 4 | 16.00 | 1.00 | 16.00
Likely | 5 | 20.00 | 0.75 | 15.00
Arguable | 7 | 28.00 | 0.50 | 14.00
Suspect | 2 | 8.00 | 0.25 | 2.00
Opposite | 0 | 0.00 | -1.00 | 0.00
Wrong | 6 | 24.00 | 0.00 | 0.00
None | 1 | 4.00 | 0.00 | 0.00
Total | 25 | 100.0 |  | 47.00
Comprehension of Exit Signs In Low (0.50) fc Lighting

## Slide 50
Comprehension Category | Frequency | Percent | Weight | Comprehension Score
Certain | 4 | 16.00 | 1.00 | 16.00
Likely | 3 | 12.00 | 0.75 | 9.00
Arguable | 9 | 36.00 | 0.50 | 18.00
Suspect | 6 | 24.00 | 0.25 | 6.00
Opposite | 0 | 0.00 | -1.00 | 0.00
Wrong | 2 | 8.00 | 0.00 | 0.00
None | 1 | 4.00 | 0.00 | 0.00
Total | 25 | 100.0 |  | 49.00
Comprehension of Exit Signs In High (45 fc) Lighting

## Slide 51
Comprehension Category | Frequency | Percent | Weight | Comprehension Score
Certain | 32 | 32.00 | 1.00 | 32.00
Likely | 12 | 12.00 | 0.75 | 9.00
Arguable | 23 | 23.00 | 0.50 | 11.50
Suspect | 16 | 16.00 | 0.25 | 4.00
Opposite | 0 | 0.00 | -1.00 | 0.00
Wrong | 15 | 15.00 | 0.00 | 0.00
None | 2 | 2.00 | 0.00 | 0.00
Total | 100 | 100.00 |  | 56.50
Overall Comprehension of Self-Illuminated Exit Signs

## Slide 52
Comprehension Category | Frequency | Percent | Weight | Comprehension Score
Certain | 19 | 19.00 | 1.00 | 19.00
Likely | 17 | 17.00 | 0.75 | 12.75
Arguable | 19 | 19.00 | 0.50 | 9.50
Suspect | 9 | 9.00 | 0.25 | 2.25
Opposite | 0 | 0.00 | -1.00 | 0.00
Wrong | 16 | 16.00 | 0.00 | 0.00
None | 20 | 20.00 | 0.00 | 0.00
Total | 100 | 100.0 |  | 43.50
Automatic External Defibrillator Comprehension

## Slide 53: Conclusions
Comprehension of small symbolic exit signs equivalent to that of signs tested for larger transport category airplanes
Use the ISO 7010:2011 running man element combined with the narrow arrows (same as approved for large transport airplanes)
The distance between any viewer inside the transport airplane cabin and these smaller exit signs should not exceed 20 feet
Standardization of symbolic exit signs for all transport airplanes will produce better comprehension by passengers