## Slide 1: Inflatable Emergency Equipment:
Evaluation of Individual Inflatable Life Preserver Donning Tests, Part 1
7th Triennial International Aircraft Fire and Cabin Safety Research Conference
Cynthia L. Corbett, MA
December 4, 2013

## Slide 2: Thank You to
Cabin Safety Research Team
  David B. Weed, MA
  David J. Ruppel,
  Ken Larcher, MAS
  G. A. McLean, PhD

## Slide 3: Background
US Airways Flight 1549 emergency landing in the Hudson River, Weehawken, NJ, January 2009
  Most of the passengers did not pay attention to the oral preflight safety briefing or read the safety information card, indicating that more creative and effective methods of conveying safety information to passengers are needed (A-10-86).
  Of the estimated 33 passengers (N = 150) who reported eventually having a life preserver, only 4 confirmed that they were able to complete the donning process by securing the waist strap themselves. Current design standards in TSO-C13f do not ensure that passengers can quickly or correctly don life preservers (A-10-85).

## Slide 4
Technical Standard Order (TSO) C13f Donning Test
  Actual/simulated coach class seating with row in front of subjects creating maximum 31” seat pitch
  Subject must begin with seat belt fastened and may release and rise from seat but must remain in front of seat
  No donning information other than typical preflight briefing and donning demonstration
  25-second time limit
    Starts when subject has both hands on packaged life preserver
    Stops when life preserver is properly donned, secured, adjusted for fit
  75% of total number of test subjects must “pass”

## Slide 5
SAE Aerospace Standard (AS) 1354 – Individual Inflatable Life Preservers
  SAE S-9 Cabin Safety Provisions Technical Committee
  Request by FAA to support TSO revision
  Process began in 2004
  “No donning information other than typical preflight briefing and donning demonstration”
  If passengers are not going to pay attention to a preflight briefing in actuality, then it should not be included in the donning test method…

## Slide 6: Research Design

## Slide 7: Research Design
Total N = 156

## Slide 8: Briefing Card Illustration for Condition C
Airline Name: USA 3000 Airlines
Equipment: A320
Designer: Interaction Research Corporation
Date of Copyright: 2005

## Slide 9: Procedure

## Slide 12: Life Preservers
Life Preserver “Q”
Life Preserver “R”

## Slide 13: Life Preservers
Life Preserver “S”
Life Preserver “T”

## Slide 14: Life Preservers
Life Preserver “U”
Life Preservers “V, W, X”

## Slide 15: Life Preservers
Life Preserver “Y”
Life Preserver “Z”

## Slide 16: Participants
 | Donning Instruction Condition |  |  |  |  | 
 | A* | BA* | B* | C* | D* | Overall
Gender | 54 | 30 | 24 | 24 | 24 | 156
Male | 57.4% | 60.0% | 12.5% | 37.5% | 33.3% | 44.2%
Female | 42.6% | 40.0% | 87.5% | 62.5% | 66.7% | 55.8%
Mean Age in Years | 46.7 | 50.2 | 48.3 | 47.5 | 41.3 | 46.9
Minimum | 25 | 24 | 23 | 28 | 26 | 23
Maximum | 75 | 66 | 68 | 62 | 61 | 75
Mean Girth in Inches | 34.8 | 37.7 | 36.5 | 38.5 | 36.4 | 36.4
Minimum | 20 | 29 | 27 | 31 | 27 | 20
Maximum | 50 | 47 | 49 | 50 | 49 | 50
Mean Height in Inches | 67.8 | 68.0 | 64.8 | 66.3 | 67.9 | 67.2
Minimum | 59 | 59 | 59 | 60 | 63 | 59
Maximum | 76 | 76 | 73 | 71 | 74 | 76
Mean Weight in Pounds | 183.5 | 201.6 | 172.9 | 188.8 | 183.0 | 186.1
Minimum | 115 | 139 | 124 | 128 | 110 | 110
Maximum | 356 | 300 | 246 | 319 | 282 | 356
*A: No instructions |  |  |  |  |  | 
*BA: Instructions on Life Preserver with no direction |  |  |  |  |  | 
*B: Instructions on Life Preserver with direction |  |  |  |  |  | 
*C: Instructions on Life Preserver and Briefing Card |  |  |  |  |  | 
*D: Instructions on Life Preserver with Briefing/Demonstration |  |  |  |  |  | 

## Slide 17: Life Preserver Experience (Pre-Test)
81.4% had traveled on a plane where the use of life preservers were explained or demonstrated
Of those, 76.9% said they DID pay attention to the explanation/demo
66% considered the explanation/demo to be adequate should they have needed to use the life preserver
85.9% had used a life preserver in connection with water activities like water skiing or boating
Of those, time since last use ranged from 1 week to 20 years or more
Most often used: Non-inflatable 74%, Auto-inflate 6%

## Slide 18: Time Measurement
TSO Time – Both hands on package, ready to open, to final adjustment
  102/156 (65.4%) Correct dons
  13/156 (8.3%) Correct don AND passed TSO Time requirement of 25 seconds

## Slide 20: Time Measurement
TSO Time – Both hands on package, ready to open, to final adjustment
Package Opening Time – Both hands on package, ready to open, to hand entering package
Donning Time – Both hands on life preserver to final adjustment

## Slide 21: Package Opening
Notes: Boxplot: Median, box (hinges) bracket the middle 50% of the scores
Whiskers contain adjacent values +/- 1.5 (hinge spread)
Outliers or extreme values

## Slide 22: Donning Time without Package Opening

## Slide 23
A: No Instruction Condition; Type S and U

## Slide 26
BA: Vest Only Instruction Condition; Type Y

## Slide 28
C: Vest and Briefing Card Instruction Condition; Type S

## Slide 30
D: Vest and Briefing/Demo Instruction Condition; Type R

## Slide 31: Overall

## Slide 34: All Instruction Conditions Follow-Up Questions
51.9% said they experienced difficulties in donning the life preserver
Primary Sources of Difficulty
  Opening the package
  Determining front and back
  Fastening/Unfastening/Adjusting waist strap (rubber band)
  Upside-down instructions on life preserver
  Neck opening too small

## Slide 35: Conclusion & Recommendations
None of the life preservers tested passed the certification criteria.
Test methods should be more explicit to better control the test environment.
Package opening should be a separate test with participants having cold/gloved hands.
A “critical” donning time should be determined.
Standards should be improved to address the difficulties identified.
Improve Passenger Safety Awareness!

## Slide 36: Publications available from: http://www.faa.gov/data_research/research/med_humanfacs/oamtechreports/

## Slide 37: Inflatable Emergency Equipment:
Evaluation of Individual Inflatable Life Preserver Donning Tests, Part 2
7th Triennial International Aircraft Fire and Cabin Safety Research Conference
Cynthia L. Corbett, MA
December 4, 2013

## Slide 38: Life Preservers
Life Preserver “Q”
Life Preserver “R”

## Slide 39: Life Preservers
Life Preserver “S”
Life Preserver “T”

## Slide 40: Life Preservers
Life Preserver “U”
Life Preservers “V, W, X”

## Slide 41: Life Preservers
Life Preserver “Y”
Life Preserver “Z”

## Slide 42: The Details…

## Slide 43: Life Preserver Donning
Correct Dons was significantly associated with Type of Life Preserver: Χ2 (7, N = 156) = 16.05, p = .025
  Type A and Z each had the highest percentage of Correct Dons (83%) followed by Type T (80%)
  Type U had the lowest percentage of Correct Dons (33%)
Pass/Fail was not significantly associated with the Type of Life Preserver
  BUT Type Y had the highest percentage of Passes (25%) followed by Type T (17%)

## Slide 44: Instruction Condition A: No Instructions/No Markings
F (4, 49) = 6.46, p < .01

## Slide 45: Instruction Condition (A/BA/B/C/D) X Life Preserver (Q/R/S/T)
No significant differences among life preservers
No significant interaction of main effects
P < .01

## Slide 46: Participants
Age was significantly correlated with both TSO Time and Donning Time (with/without package opening), but…r = .289, p < .001
No other participant physical characteristics were significantly associated with Donning Time

## Slide 47: Flight Experience
Number of Flights taken in the past year was significantly correlated with TSO Time and Donning Time
  r = -.20, p = .02
  r = -.18, p = .04
Within 25 seconds
  Pass average 14.3 flights
  No Pass average 3.9 flights

## Slide 48: Time spent reading markings
No significant difference in mean time reading markings on Life Preserver between B (with direction) and BA (without direction)
  B: 1.43 to 34.03 seconds, M = 13.32
  BA: 0 to 39.73 seconds, M = 10.51
    Years of education significantly correlated with Total Time Spent Reading Markings, r = -.391, p = .03
No significant difference among Life Preservers
  Q: 8.54
  R: 12.64
  S: 15.08
  T: 13.85
  Y: 5.63 (BA Condition Only)

## Slide 49: All Instruction Conditions Follow-Up Questions
51.9% said they experienced difficulties in donning the life preserver
28.2% reported they would have done worse, and 64.7% reported they would have done about the same if this had been an actual emergency aboard an airplane
36.5% said they would not have felt confident in their preparedness for an actual over-water evacuation

## Slide 50: Primary Sources of Difficulty
Opening the package
Determining front and back
Fastening/Unfastening/Adjusting waist strap (rubber band)
Upside-down instructions on life preserver
Neck opening too small

## Slide 51
47% said they read the instructions on the equipment or package
48% stated that they experienced confusion or uncertainty in following the instructions
How useful were instructions in helping you don the life preserver?
  BA 30% Adequate, 37% Marginal, 30% Inadequate
  B 63% Adequate, 29% Marginal, 8% Inadequate
  C 75% Adequate, 25% Marginal
  D 83% Adequate, 13% Marginal, 4% Inadequate
Instruction Conditions
**May not total 100% due to rounding or no response

## Slide 52
How well do you think you would have done if no information had been given?
  BA 7% Better, 57% About same, 33% Worse
  B 4% Better, 50% About same, 46% Worse
  C 0% Better, 58% About same, 42% Worse
  D 4% Better, 29% About same, 67% Worse
**May not total 100% due to rounding or no response

## Slide 53: Recommendation
“If passenger safety is to be improved through the use of existing TSO devices, it will probably have to be achieved through a stronger than usual emphasis on correct usage during passenger briefings and require more than passive or elective attention by the passengers.”
      Rasmussen and Steen (1983)

## Slide 54: Publications available from: http://www.faa.gov/data_research/research/med_humanfacs/oamtechreports/